## Slide 1
Automated Control system for a Small-scale Green House
200313P
200314U
200315A

## Slide 2
Light
Intensity
Temperature
Moisture
Make a way to reduce Light effect
Make a way to reduce temperature
Make a way to Dryness

## Slide 3
We built a Light sensor using a LDR
Measured the variation of Voltage across the LDR using a Multimeter with the Light intensity using a LUX meter
Plot the variation and we get a power Equation and we calibrate it
We get the equation as follows

## Slide 4
Lux | V
270 | 3.52
120 | 3.93
1.3 | 4.96
185 | 3.76
90 | 4
440 | 2.93
600 | 2.63
700 | 2.5
1009 | 2.3
1300 | 2.16
2900 | 1.64
4020 | 1.47
105000 | 0.41
23067 | 0.84
17000 | 1.45
22000 | 0.76
7000 | 1.14
12500 | 1.13
40500 | 0.57
80000 | 0.51
60000 | 0.69
50000 | 0.54
40000 | 0.63
20000 | 0.83

## Slide 5
Chart: variation of voltage across the LDR(y) with Light intensity (x)
| 270 | 120 | 1.3 | 185 | 90 | 440 | 600 | 700 | 1009 | 1300 | 2900 | 4020 | 105000 | 23067 | 17000 | 22000 | 7000 | 12500 | 40500 | 80000 | 60000 | 50000 | 40000 | 20000
 | 3.52 | 3.93 | 4.96 | 3.76 | 4 | 2.93 | 2.63 | 2.5 | 2.3 | 2.16 | 1.64 | 1.47 | 0.41 | 0.84 | 1.45 | 0.76 | 1.14 | 1.13 | 0.57 | 0.51 | 0.69 | 0.54 | 0.63 | 0.83

## Slide 6
y = 11.928 x -0.262
X=Light intensity
Y=Voltage across the LDR
Sensor formula is

## Slide 7
In the controlling part of Light we use a Logic Gate to connectivity
Light intensity is high = L (1)
Light intensity is Low= L (0)
Ultra sonic 1 detect the screen =A(1)
Ultra sonic 1 detect the screen =A(0)
Ultra sonic 2 detect the screen =B(1)
Ultra sonic 2 detect the screen =B(0)

## Slide 8
L | A | B | In 1 | In2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 |  | 
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 |  | 
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0
Hypothetical cases
Forward
reverse
Off
Off